| UNC Modification | At what stage is this document in the process? |
| --- | --- |
| UNC 0XXX: Updating the Offtake Arrangements Document (OAD) with recommendations resulting from UNC Request Workgroup 0646R – Phase 1 |  |
| Purpose of Modification: This Modification seeks to update the OAD in order to bring it in line with industry changes made since 2005. UNC Request Workgroup 0646R was formed in March 2018 with representation from all Network Operators to review the current OAD. The Workgroup has since identified a number of areas in OAD that can be updated now (Phase 1), with the remainder to be considered under a future Modification (Phase 2). |
|  | The Proposer recommends that this modification should be: Self-Governance and proceed to Workgroup This modification will be presented by the Proposer to the Panel on 20th December 2018. The Panel will consider the Proposer’s recommendation and determine the appropriate route. |
|  | High Impact: NG UKT and all GDN’s. |
|  | Medium Impact: None |
|  | Low Impact: None |

| Contents 1 Summary 3 2 Governance 3 3 Why Change? 4 4 Code Specific Matters 6 5 Solution 6 6 Impacts & Other Considerations 7 7 Relevant Objectives 8 8 Implementation 9 9 Legal Text 9 10 Recommendations 9 11 Appendix 9 Timetable The Proposer recommends the following timetable: Modification presented to Panel 20 December 2018 Modification considered by Workgroup 22 January 2019 Workgroup Report presented to Panel 21 February 2019 Draft Modification Report issued for consultation 22 February 2019 Consultation Close-out for representations 14 March 2019 Final Modification Report available for Panel 21 March 2019 Modification Panel decision 21 March 2019 | Any questions? |
| --- | --- |
|  | Contact: Joint Office of Gas Transporters |
|  | enquiries@gasgovernance.co.uk |
|  | 0121 288 2107 |
|  | Proposer: Shiv Singh |
|  | shiv.singh1@cadentgas.com |
|  | 07580 999 287 |
|  | Transporter: Cadent |
|  | shiv.singh1@cadentgas.com |
|  | 07580 999 287 |
|  | Systems Provider: Xoserve |
|  | UKLink@xoserve.com |
|  | Other: Darren Dunkley |
|  | Darren.dunkley@cadentgas.com |
|  | 07768 102 196 |

# Summary

#### What

Since the implementation of the OAD in 2005, a number of issues have been identified that need to be addressed. A series of amendments were identified during the development of Request 0646R, a number of which it has been identified can be addressed at an early stage. This Modification Proposal is described as Phase 1 and addresses:

- Tripartite arrangements;

- Shared Sites (including the definitions: for bi-directional/reverse flow; and Closed Sites NTS/LDZ);

- Asset Removal process; and

- Supplemental Agreement Template

#### Why

In its current form, sections of OAD are unclear and ambiguous. As a result, it is open to interpretation which has at times resulted in an inefficient use of both time and resource of the parties concerned. The proposed changes would enable all parties to interpret a Code that is clear, concise, practical and consistent.

#### How

The relevant sections of OAD are proposed to be amended, with where required, new additions included, so that the resultant legal text satisfies the objectives of the Proposal.

The sections of OAD to be modified include:

- Section A – Scope and Classification

- Section B – Connection Facilities

- Section N – General, and

- Appendix Supplemental Agreements

# Governance

#### Justification for Self-Governance

This Modification should be subject to Self-governance procedures on the basis that the necessary changes would have no material impact on the commercial activities of Shipper Users, Gas Transporters or Gas Consumers. This is because the proposed changes are to either bring the Code in line with industry changes since 2005, or to address process gaps that have come about as a result of new industry practice.

#### Requested Next Steps

This Modification should:

- Proceed to Workgroup to review legal text and produce a Workgroup Report

# Why Change?

#### Background

Since the implementation of the OAD in 2005, a number of issues have been identified which need to be addressed. It has been identified that specific sections of OAD are unclear and ambiguous and require clarity to ensure all parties are able to interpret them in a consistent manner. By not addressing these issues, parties may continue to apply different interpretations, on occasions resulting in an inefficient use of time and resource. The 0646R Workgroup has agreed that a number of changes to OAD should be made as part of Phase 1. These cover:

- Tripartite arrangements;

- Shared Sites (including the definitions: for bi-directional/reverse flow; and Closed Sites NTS/LDZ);

- Asset Removal process; and

- Supplemental Agreement Template

Further Phase 2 Modifications are anticipated in a separate Modification in 2019 to cover:

- Critical National Infrastructure (Integrated Security System(ISS)/Physical Security Upgrade Programme(PSUP));

- Maintenance (and clarity on impact assessments/threshold for OAD notices “significant impact” Section G);

- Site Drawings;

- OAD Notices;

- Point of Offtake.

The 0646R Workgroup also recognised that additional areas for related Offtake Arrangements work in 2019 is expected to include:

- Section D; and

- SCO interface documents.

#### It is still to be determined whether these items will be addressed by the existing 0646R Workgroup or by the Offtake Arrangements Workgroup, and whether they will be addressed in Phase 2, or at a later stage.

#### The Detail

Tripartite Arrangements

Section A 2.1.2 & A 2.3.1

1. Cadent has two tri-party sites where there is one Site Owner and two Site Users located at an offtake. OAD is currently written in a way that assumes there is only one Site Owner and one Site User, and that gas flows from the NTS into one LDZ. In reality, this is not the case and the definitions need to be updated to cover both approaches.

a) Offtake definition i.e. "one or more Individual Offtakes Points, located at each site, at each of which gas can flow into the same LDZ." does not cater for tri-party sites.

This may also impact upon Section A 2.3.1.

Section B 2.6.1

2. Site Services need to be revised to take into account tri-party sites. Normally, there are two Supplemental Agreements (SA) in place between the upstream and downstream operators. However, as the GDNs are normally the Site Owners, one SA will be between the Site Owner and Site User, and the other SA will be between the Site User and Site User. Where a SA is between two Site Users, the Site Services are not confirmed by the Site Owner as they are not a party to the agreement. Therefore the two Site Users are unable to agree these services without the Site Owner.

a) The "Services Party" can be a third operator who is the Site Owner but not a party to the Supplemental Agreement because this is between the upstream and downstream party only - as in the case at Ross-on-Wye and Winkfield (i.e. tri-partite sites).

New Addition

3. There have been occasions for tri-party sites where one SA has been updated between the Site Owner and Site User, but the changes have not been mirrored across to the other SA in place between the Site User and Site User. This is critical for issues where for example there are data items that are common between the two SA's in place, such as access, security, cathodic protection, utilities supply and drawings i.e. GA and HAZ resulting in a mismatch of data between the two SA's.

a) Section N does not contain any clauses outlining that National Grid are the custodians of the Supplemental Agreements.

Shared Sites

Section A 2.1.4

1. Cadent has a specific site where the systems are connected by closed valves and if opened gas could flow.   This site is not covered by a Supplemental Agreement.

a) Offtake Definition does not allow for closed NTS/LDZ offtakes that have the potential to flow gas.

New Addition

2. Offtake sites are governed by OAD but, due to the current offtake definition in Clause A2.1.4, it only covers where gas flows from the NTS into an LDZ. Cadent have a number of offtake sites where a connection back onto the NTS is required to facilitate pipeline inspections that only occur once every 10-15 years.

Asset Removal Process

Section B 3.1.1

1. Clause states that "right to the Site User to retain such Connection Facilities on the Site Owner land." as per the date of the SA or following relocation.   The issue here is that this right allows the Site User to leave assets in place even though they are not operational and there are no clauses in OAD that allow the Site Owner to request the removal of redundant assets so it frees up land for other use.

Section B 3.6

2. This clause focuses on the Removal of Site User Facilities from only a Site User perspective. OAD provides no coverage for Site Owners to request the removal of Site Users assets, especially redundant assets given the right to retain stated in B3.1.1.

The ‘Proposal for the Removal of Assets v0.4’ is included in Appendix 1.

Supplemental Agreement Template

Section B 2.1.2

1. The current version of the SAs does not 'specify' all the Connection Facilities in Appendices C and D. These are also contained within Appendix E.

New Addition

2. A General point: The SA's should have version control so that you are able to see what changes were implemented when, and arising from what work.

a) No version control for SA’s.

The ‘SA Appendix Template v1.0 – Blank’ is included in Appendix 2.

Appendix

3. Current Supplemental Agreements do not document all of the Connection Facilities on site, as per Section B of OAD. Specifically, whilst the mechanical drawing is included with the SA, there is no mention of the electrical assets on site which often can be shared and therefore lead to confusion as to who owns them and thus, maintains them.

a) Appendix SA to be revised to the new OAD Pack.

# Code Specific Matters

#### Reference Documents

Offtake Arrangements Document (found here: https://www.gasgovernance.co.uk/OAD)

#### Knowledge/Skills

An understanding of physical assets, access arrangements, etc would be advantageous.

Solution

Tripartite Arrangements

Section A 2.1.2 & A 2.3.1

To be amended to cater for tri-party sites.

Section B 2.6.1

B 2.6.1 to be revised to state that the "Services Party" must be named in the Supplemental Agreement, and recognised as the Site Owner and has a presence on site.

B 2.6.2 to be revised to include sub-clause (d), where the Site Owner is neither the upstream nor downstream party named in the SA.

New requirement

Section N

As National Grid are the custodians of the SA's, then additional requirements are needed to maintain the integrity of information between SA documents for where there is more than one offtake at a location including tri-party sites. If one document is updated, they should have a duty to inform all other Operators highlighting the changes that need to be made to any remaining SA’s.

Shared Sites

Section A 2.1.4

The definition for Offtakes needs to be expanded to cover a number of scenarios:

- The existing definition;

- Closed NTS to LDZ offtakes;

- Bi-directional NTS to LDZ offtakes (limited to certain sites only); and

- Shared sites with no physical connection via Individual Offtakes Point(s).

Note: For point 1 above, the existing definition from A 2.1.4 does not need to change as it is still valid.

Asset Removal Process

Section B 3.1.1 and B 3.6

Sections B 3.1 and B 3.6 need to be reviewed to accommodate the process agreed by the Operators. This can be found in Appendix 1, entitled ‘Proposal for Removal of Assets v0.4’. Insert the necessary additional clauses to accommodate this new process.

Note: Other GDNs have Lease Agreements in place with NG concerning their offtakes. These agreements have greater legal precedence than OAD and therefore, any amendments to the clauses needs to ensure the Operator follows the correct Terms and Conditions before continuing with the asset removal process.

Supplemental Agreement Template

Section B 2.1.2

The Section of OAD entitled ’01 January 2006 OAD Appendices’ is to be removed and set up as a subsidiary document as follows:

- Recitals (see Appendix 2: Supplemental Agreement Template); and

- Appendices (see Appendix 2: SA Appendix Template v1.0 – Blank)

There are many references in OAD to the Supplemental Agreements and the OAD needs to be reviewed and updated accordingly, taking into account this important document is now a subsidiary one.

Impacts & Other Considerations

#### Does this modification impact a Significant Code Review (SCR) or other significant industry change projects, if so, how?

There is no impact on any Significant Code Review.

#### Consumer Impacts

There is no impact on consumers on the basis that the Modification is solely associated with Transporter to Transporter issues.

#### Cross Code Impacts

No other industry codes are affected.

#### EU Code Impacts

There is no impact on any EU Code.

#### Central Systems Impacts

There is no impact on any central systems.

Relevant Objectives

| Impact of the modification on the Relevant Objectives: |
| --- |
| Relevant Objective | Identified impact |
| a) Efficient and economic operation of the pipe-line system. | Positive |
| b) Coordinated, efficient and economic operation of (i) the combined pipe-line system, and/ or (ii) the pipe-line system of one or more other relevant gas transporters. | Positive |
| c) Efficient discharge of the licensee's obligations. | None |
| d) Securing of effective competition: (i) between relevant shippers; (ii) between relevant suppliers; and/or (iii) between DN operators (who have entered into transportation arrangements with other relevant gas transporters) and relevant shippers. | None |
| e) Provision of reasonable economic incentives for relevant suppliers to secure that the domestic customer supply security standards… are satisfied as respects the availability of gas to their domestic customers. | None |
| f) Promotion of efficiency in the implementation and administration of the Code. | Positive |
| g) Compliance with the Regulation and any relevant legally binding decisions of the European Commission and/or the Agency for the Co-operation of Energy Regulators. | None |

This Modification facilitates GT Licence relevant objective a) Efficient and economic operation of the pipe-line system and b)(i) Coordinated, efficient and economic operation of the combined pipe-line system as it provides clarity on OAD matters impacting the Gas Transporters, thus enabling effective communication between parties, and a more efficient use of assets contained within their Systems.

This Modification also facilitates GT Licence relevant objective f) Promotion of efficiency in the implementation and administration of the Code by providing clarity in the UNC regarding Tripartite Arrangements, Shared Sites, Asset Removal, and Supplemental Agreements.

Implementation

As self-governance procedures are proposed, implementation could be sixteen business days after a Modification Panel decision to implement, subject to no Appeal being raised.

Legal Text

#### Text Commentary

Text to follow

#### Text

Text to follow

Recommendations

#### Proposer’s Recommendation to Panel

Panel is asked to:

Issue this Modification to Workgroup to review Legal Text and produce a Workgroup Report

Appendix

#### Appendix 1

#### Appendix 2

# Text boxes

Guidance on the use of this Template:

Please complete all sections unless specifically marked for the Code Administrator.

Green italic text is provided as guidance and should be removed before submission.

The Code Administrator is available to help and support the drafting of any modifications, including guidance on completion of this template and the wider modification process. Contact: enquiries@gasgovernance.co.uk or 0121 288 2107.