## Slide 1: UNC Modification Proposal 0202 National Grid Distribution
“Improvement to More Frequent Readings Provisions to allow benefits of AMR”
Distribution Workstream – 28 February 2008
Chris Warner

## Slide 2: Introduction
Current Frequency
Proposal and Read Volume Implications
Benefits
Smart Metering – Policy Direction
Summary

## Slide 3: Current More Frequent Reading Provisions
TPD Section M3.7 (Mod 0693 – Nov 2005)
  Monthly Read Meter – one read each 7 day period
    52 readings per year
  Annual Read Meter (Larger Supply Point) – one read each 14 day period
    26 readings per year
  Annual Read Meter (Smaller Supply Point) – one read each 63 day period
    5.8 readings per year
Previous frequencies (pre 0693)
  Monthly Read Meter – min 23 days from previous reading
    15.9 readings per year
  Annual Read Meter – min 5 months from previous reading
    2.4 readings per year

## Slide 4: Proposal
TPD Section M3.7 (Mod 0693 – Nov 2005)
  Monthly Read Meter – one read each 7 day period
    52 readings per year
  Annual Read Meter (Larger Supply Point) – one read each 14 day period
    26 readings per year
  Annual Read Meter (Smaller Supply Point) Domestic flag – one read each 63 day period
    5.8 readings per year
  Annual Read Meter (Smaller Supply Point) Non-domestic flag – one read each 27 day period
    13.5 readings per year

## Slide 5: Read Volume Implication
Jan 2008 – 381,859 SSP meters flagged non-domestic
Current maximum frequency 1 in 63 day period
  (365/63)*381,859 = 2,212,358 (annually)
  6,061 (average daily)
Proposed maximum frequency 1 in 27 day period
  (365/27)*381,859 = 5,162,168 (annually)
  14,143 (average daily)
Potentially a 8,000 read increase on ‘contractually allowable’ daily read volumes

## Slide 6: Suggested Benefits
Improvement to gas profiling and allocation by GTs due to a more detailed read history
  Annual Quantity (AQ)
    single annual figure derived from a single pair of reads at least six months and 1 day apart, no more than 3 years apart
    sum of consumptions for the period, weather-adjusted back to seasonal normal temperatures and corrected to 365 days
    further reads between those two “calculation reads” do not contribute to the quality of the AQ
  AQ determines EUC
    gas allocation based on a single annual load profile for the EUC
    derived from the Demand Estimation Process and the NDM Sample
    does not rely on historic meter reads
  Potential benefits to allocation of sites to Winter Annual Ratio (WAR) bands
    However WAR bands are only applicable to Supply Points with AQ > 293,000kWh

## Slide 7: Benefits to User - Assumptions
Enables User systems to deliver readings directly to the Transporter
  For I&C portfolio single read frequency (monthly) can be set
  Therefore no ‘filtering’ required to meet existing read frequency requirements for SSP
  Any others?

## Slide 8: Smart Metering – Policy Direction
BERR - Energy Billing and Metering (Energy White Paper) - proposals
  installation of smart meters/AMR for business customers above a certain energy usage threshold (gas consumer >73,200kWh), where it has been proven to be cost effective – within 5 year period
  Installation of smart meters at remaining small business & domestic (<73,200kWh) premises within next 10 years - 3 policy options being debated
    New and replacement
    Competitive market
    10 year roll out
  additional question regarding impact on industry settlement processes and codes
Decision document due Q1 2008

## Slide 9: Summary
Increases the maximum volume of reads able to be submitted to the Transporter by average of 8,000 per day
No benefit to UNC processes
  profiling and allocation at Smaller Supply Points
  to reconciliation of Smaller Supply Points
  AQ derivation
Potential benefits for Users?
Ongoing industry consultation